## Slide 1: Experience in Photo-Detection DAQ from the SoLiD Neutrino Experiment
David Cussans, University of Bristol
Second UK-Latin America Workshop on DAQ and Data Selection
Bogota, Colombia
13/November/2018

## Slide 2: Outline
Experience of designing the readout electronics for a small ( 3200 channels ) short baseline neutrino detector.
  How design is driven by resources and history as well as the functional requirements.
Some remarks on (proto)DUNE SP Photon Detection System (PDS)
Summary

## Slide 3: SoLiD Short Baseline Neutrino Detector
Aims:
  Set limits (discover) sterile neutrino
  Investigate neutrino energy spectrum in region of 5MeV
  Demonstrate technology useful for reactor monitoring (treaty compliance)

## Slide 4: The Reactor Anomaly
Calculations of reactor spectrum show persistent 2.7σ deficit in previously measured rates at distances between 9 m and 1 km (JHEP 1305:050)
Now been reassessed….

## Slide 5: The 5MeV Bump
5 MeV n excess
  Daya Bay
  Double Chooz
  RENO
All Gd doped liquid scintillator
All low enriched Uranium power reactors
SoLiD at BR2, with different isotopic composition

## Slide 6: Reactor Monitoring
Reactors produce Plutonium
Aim to detect diversion for weapon production
Pu ν̄e spectrum softer than U
  Spectrum sensitive to isotopic composition
Current treaty verifications methods measure power
  Hard to recover from loss of measurement
Neutrino detectors can significantly reduce uncertainty in quantity of Plutonium removed from a reactor
PRL 113, 042503

## Slide 7: SoLiD at BR2
BR2 Ideal for short baseline reactor neutrino experiment
  Small core ( 50cm diameter )
  Well know isotopic composition
  Short baseline ( ~ 6 m)

## Slide 8: Neutrino Detection – Two scintillators
Use inverse beta decay:
  νe + p → e+ + n
e+ usually contained in single cube
Annihilation γ scatters outside cube
Neutron thermalizes and is absorbed in 6Li

## Slide 9: Neutrino Detection – Two Scintillation TImes
Absorption of neutron in 6Li , emission of α, scintillation in ZnS. Long time-scale, τ ≈ O(us) .
e+ scintillates in PVT as it slows to a halt τ ≈ O(ns ).

## Slide 10: Detection Volume and Optics
Detector split into vertical planes
  Segmentation helps identify and reduce background
Optically isolated scintillator cubes
  16 × 16 cubes per plane
  32 vertical and 32 horizontal fibres
  3 × 3 mm square WLS fibres
  3 × 3 mm square MMPC (SiPM)
50 planes total
  12.8k cubes
  3200 readout channels
      c.f. 6000 in baseline DUNE SP PDS

## Slide 11: Light Sensors – MPPC (SiPM)
Silicon photomultiplier
3 × 3 mm active area
3600 parallel Geiger mode APDs
Charge sum from number of pixels that avalanche
Operating voltage < 70 V
Temperature dependant breakdown voltage
High dark count rate (MHz @ single pixel)
Cross talk (10 - 30%)
Twisted pair –
2 signal wires,
2 “shield” wires

## Slide 12: Single Plane: Data Flow

## Slide 13: Readout Hardware
Constrained budget: time and money , so:
  Modular electronics: Fewer system-level effects.
  COTS FPGA module ( with Xilinx Artix-7 200) at heart of custom 64-channel ADC + readout board
Used IPBus for readout over UDP/IP
  See https://ipbus.web.cern.ch/ipbus/
  Firmware utilities (ipbb build system, simulation framework) very useful
Separate amplifier board (with SiPM bias)
  Allowed division of design and testing.
Differential connection to SiPM
  low cost, rapid termination
    … but not usable at cryogenic temperatures)

## Slide 14: Readout Hardware

## Slide 15: Pulse Shapes

## Slide 16: Grounding and Shielding
Mechanical frame round cubes is hollow.
  Electrically connected to form Faraday cage.
Single electrical connection between frame and amplifier.
Separate enclosure for each plane of cubes
Twisted pair cable.
  Extra wires act as a “screen” - connected to “ground plane” on SiPM PCB

## Slide 17: Firmware
Firmware highly efficient to make use of low cost FPGA

## Slide 18: Readout Software
Readout software written in “Go lang”
  Language developed by Google
  Excellent parallel programming constructs
Issues:
  No interface to IPBus available for “Go”. Had to be written
    Subtle incompatibilities resulted in frequent subtle bugs
  Only one person in collaboration familiar with Go.
    …. And they left for another job

## Slide 19: System Costs

## Slide 20: First version readout
Designed by a team that then had to leave the project due to movement of personnel / funding issues.
Front end based on existing design
  See The front end readout system for the T2K-ND280 detectors
    Successfully used for ECAL, the SMRD (side muon range detector), the P0D (pi-zero detector) and the INGRID (the cross that is measuring the beam pointing).
  Used coaxial cable with voltage trim on shield
SoLiD SM1 prototype readout worked acceptably well on bench with small number of channels.

## Slide 21: T2K-ND280 / SoLiD Analogue Front End
ND280
SoLiD SM1

## Slide 22: SoLiD SM1 performance
Many channels: Oscillation !
  1 Pixel Avalanche ~ 20 ADC counts. Buried by oscillation
  Marginal phase stability. Cross talk seems to induce oscillation
U/FL cables high performance, but mechanically awkward
  160 cables already problematic to install

## Slide 23: Some comments on scaling
SM1 (20% prototype) very useful to find out what scales (from few channels) and what doesn’t.
  E.g. Cabling
”Iceberg” small test-setup will be very useful
NA62 RICH
( 1000 cables per sector)
( Chris Parkinson)

## Slide 24: SM1 → Phase 1
Bristol joined SoLiD after SM1 readout architecture decided
  Very limited budget ( SoLiD not supported by UK funding agency )
  Amplifier + ADC for SM1 already produced.
    Combined with CMS “GLIB” board to produce readout system
Very limited time ( other experiments also moving towards making measurements )
Produced an 8-channel board, then 64 channel with new design.

## Slide 25: SM1 → Phase 1: Some Opinions
Always prototype – the first version always gets thrown away ….
Adding effort to an existing project causes disruption that will slow things down before it speeds them up
  See “The Mythical Man-Month”, Frederick Brook
  Brook’s Law (paraphrased) “Adding effort to a late software project makes it later”
Balancing between re-using experience and trying new things remains hard
  “Soldiers are always preparing to fight the last war” , 1934 E. P. Warner

## Slide 26: SoLiD Collaboration

## Slide 27: Summary
Be reassured – SiPM readout system O(1-10k) channels can be built by a small team on a tight budget in a hurry.
“Shielded” twisted pair cable works well for SiPMs
  But we knew this from ProtoDUNE anyway
The cost of the central digitizer is a small part of the system cost.
  Less true if analogue front end is included in ASIC